Line Following Robot
Frank Bruno	James Ihrig

University of Central Florida University of Central Florida
4000 Central Florida Blvd 4000 Central Florida Blvd
Orlando, Florida, 32816 Orlando, Florida, 32816
        fbruno13@knights.ucf.edu JEIhrig@gmail.com

Abstract
The abstract will talk about the project as a whole in no more than 150 words.
# Introduction (0.5 - 1 page) F
This is the introduction section. It should talk about our project in general and the goals, motivation, and real life applications of this project.
Goals:
SPEED
LOW ERROR

# Related Work (0.5 - 1 pages) F
This is the related work section. It should talk about the work being done that relates to this project, such as, other designs for line following robots, learning techniques, and controller methods.
# Method (2-4 total pages)
This section should talk about what we are using to make this project.
Hardware (2 pages) F
This section discusses the hardware used to make the line following robot. The focus of this section is on the design decisions made while constructing the robot such as what parts were used in creation of the robot including sensors, microcontroller (MCU), Wireless Command and Reporting, Power, and Motors. It will also cover some of the hardware limitations and the cost of the robot.

Chassis
As discussed in the related work, many line following robots are small RC car like robots. They can have 2 or more wheels. The smaller and lighter the robot the more speed the robot will have. The body of the line following robot will consist of a Pololu 5" Robot Chassis RRC04A Solid Blue base with a Pololu 3pi Expansion Kit without Cutouts – Black mounted to it (Input height) inches above. The expansion kit is essentially a prototyping board the same dimensions as the base. This chassis allows for the most flexibility to design the rest of the robot and is very light weight. Additionally, the base comes with cutouts for the wheels and many predrilled holes. This design does limit the amount of wheels to 2, but given the light weight design 2 wheels should be sufficient. Since the robot is using only 2 wheels, a Pololu Ball Caster with 3/8" Metal Ball will be used with a counter weight to keep the robot balanced. The ball will just roll as it makes contact with the surface.

Sensors
As discussed in the related work, many line following robots simply use some form of an IR led and a Photodiode used to measure the reflectance from the surface directly below the robot. This combination will output a voltage based on the level of reflectance from the surface. This voltage will be close to zero when on a white surface and close to the voltage of the input source when on a black surface. A very important choice that needs to be made is how many IR led and Photodiode pairs (sensors) will be used. This is mainly dependent on the size of the robot and the width of the tape. Ideally, the amount of sensors is as many as possible to spread across the width of the robot without the sensors interfering with each other. Since the track is made using (INPUT WIDTH OF) electrical tape, see Error: Reference source not found, the ideal width is smaller than the tape. This way more than one sensor would be able to see the tape at a time. Also, the sensor array shouldn’t be much longer than the robot which is 5 inches. Given these specifications, the ideal amount of sensors is 8 or at the worst 6.

With these specifications in mind, there are two easy choices for the sensor array the Pololu QTR-8A Reflectance Sensor Array and Pololu QTR-8RC Reflectance Sensor Array. With a good price point of only 15 dollars each, both are very good choices. The QTR-8 comes with 8 IR/Photodiode pairs and can be run at either 5 or 3.3 volts, very common voltage ratings. The spacing between each sensor is 0.375 inches. This falls in line with the required specifications. The only difference between them is the RC can be hooked up to any digital I/O and the A must be hooked up to an analog input only. Since either of them are good choices the choice of the MCU will determine, which sensor array will be chosen based on the number of analog inputs.

Motors
The motors are a very important since they will be the driving force propelling the robot forward. An important goal of this project is to create a line following robot that is very fast. Therefore, a variety of motors were researched from Pololu. All of these motors have a voltage rating of 6 volts, but will work with any voltages between 3 and 9 volts. So, they are compatible with the already chosen sensor array. Additionaly, these motors are small 0.94" x 0.39" x 0.47" and 0.35 oz. The first of which is a 50:1 Micro Metal Gearmotor HP with Extended Motor Shaft. This motor is very fast with 625 RPM, they use 100 mA when free running and 1.6 A at stall. *****This motor can 15 oz-in.***** The second is a 50:1 Micro Metal Gearmotor with Extended Motor Shaft. This motor is much slower than the previous with only 250 RPM, but they use just 40 mA when free running and 360 mA at stall. *****This motor can 6 oz-in.***** The last motor reviewed is a 100:1 Micro Metal Gearmotor with Extended Motor Shaft. This motor is the slowest of the motors reviewed with 120 RPM, they use 40 mA when free running and 360 mA at stall. *****This motor can 10 oz-in.***** Although, they are the slowest they provide more torque than the 50:1 standard motors. The ideal choice is the 50:1 HP motors because it meets our specifications better than the others, but it requires a power source that can provide up to 3.2 A if the wheels stall, and a MCU that can output at least 100mA and up to 1.6 A per motor. Since Pololu offers brackets and wheels that will fit any of the motors reviewed, the wheels for the line following robot were chosen to be a pair Pololu Wheels which are 42x19mm and the pair of brackets chosen were the Pololu Micro Metal Gearmotor Bracket Extended.

Robot Controller
With the sensors and motors chosen, the next choice is what will receive the input from the sensors and use this data to drive our motors to achieve the goal of line following. The Pololu Baby Orangutan B-328P was chosen as our robot controller. This decision was based on the fact that this robot controller uses an 8-bit Atmega328p microcontroller in a 24-pin form factor complete with headers for an easy to manage prototyping environment, which is ideal given that a prototyping board is being used. The Atmeg328p comes with the ability to drive two independent motors with a continuous current supply of 1 Amp per motor with a peak current at 3 Amps per motor. This falls in line with any motor that was discussed. Therefore, the 50:1 HP motors will be used since they provide the most speed. In addition, this MCU comes with 8 analog inputs, which is exactly how many we need for the 8 sensor inputs. Therefore, the QTR8-A sensor array will be used. Also, the recommended input voltage is between 5 – 13.5 volts.

Power
In order to power these devices, a power supply must be chosen. Additionally, the voltage must be regulated using a voltage regulator. This insures no spikes from a battery will cripple any of the components. Since all of the components have support for an input of 5 volts, 5 volts is used as the voltage for the robot. The LT1963ET voltage regulator from linear technologies is used to do the job of regulating the voltage. It can receive input voltages of ± 20 V and supply 1.5 A to the robot at any voltage from 1.21 V to 20 V. Our ideal choice for a battery is a 9 V, but due to the large supply of current required from the motors a single 9 V cannot be used. So, instead the robot uses a 12 V ??????? with capacity ????? mA/h. This allows the robot to run for a few hours.

Wireless Command and Reporting

Cost

PID controller (1 page) J
To control our robot, we have decided to use a well know method known as a PID controller. PID stands for Proportional Integral Derivative. A PID controller works based on current error, duration of error and change in error and tries to counter such error in a balanced way that results in a smooth accurate tracking. When deciding to use a PID controller, the first thing that must be decided is how to calculate the initial error. For our robot, our error is calculated by checking if each of our sensors is activated (above some threshold.). Specifically, it can be described as:

NUM_LINE_SENSORS = 8
DESIRED = 0
for ( i = 0; i < NUM_LINE_SENSORS; i++)
{
lineSensor[i] = analogRead(i)
if (lineSensor[i] > SENSOR_THRESHOLD)
{
if (i < NUM_LINE_SENSORS/2)
{
actual -= 2 * (NUM_LINE_SENSORS/2 - i)
}
else
{
actual += 2 * (i - NUM_LINE_SENSORS/2 - 1)
}
}
}
error = DESIRED - actual

Where linesSensor[i] can range between [0,1023], depending on activation level, and SENSOR_THRESHOLD is set to some value in the range [0, 1023], in our case it is 400. A simplified way to look at this is to check if each sensor is activated, if it is, then add to error if it's on the right side, subtract if it's on the left side.

Now that we have an error, we can start to construct a PID controller. The proportional component of the PID controller tells the robot to turn proportionally to the error., the integral component tells the robot to use the sum of error over time to determine how much to turn when current correction has not been enough to correct the error over time, and the derivative component tells the robot uses the rate of change of the error to dampen the turn rate to help prevent over-correction. We multiply each of these terms by some constant to tune each constant until we get good results. First we add a P value only and test it on the track, tweaking it until it seems to track with minimal oscillation, we then add a D term to dampen some of the oscillation. The I term is then added to ensure that the robot does not take turns too widely.

We have found some constants for P,I and D that yeilds some good results, but we will include some results from running other values near those that we found to show the differences that are seen when other values are used. In our tests so far, the best constants for P, I and D we have found are 25, 0.05, and 15 respectively.

This section should talk about the PID controller and how it works. It should include Explanation of the controller and terms include pseudo-code and the control system loop. Explain how we are calculating error and how the manual tuning process works for us. As well as, the values of P, I, and D we used for our default values that yielded good results.

Here is the code we used for our PID controller:

P = 25, I = 0.05, D = 15

//The P multiplicand
error = desired - actual;

//The D multiplicand
dError = (error - oldError) / (currentTime() - lastFrameTime));

//The I multiplicand
sumError += error * (currentTime) - lastFrameTime);

//Set old error to current
oldError = error;

lastFrameTime = currentTime();

//Turn rate
return P * error + I * sumError + D * dError;
Learning PID values (0.5 – 1 page) J
We have considered many different ways to learn PID values ranging from Genetic Algorithms, Neural Networks, to simple gradient descent. We have realized that since we are not running in a simulated environment, large degrees of exploring will be detrimental to our leaning process as it will cause the robot to go off course and we have no way of automatically resetting. Therefore we have mostly looked into using different forms of gradient descent that don’t explore much such as the hill climber algorithm and a tree method I came up with independently, but the hill climber seemed too restrictive and the tree method would either use too much memory, or lose some good values. In the end, we have decided to use simulated annealing to learn the values as it seemed to be the best option for searching from a known decent value and keeping memory usage low.
We have decided to attempt to learn PID values. After considering several methods, we have decided that simple gradient descent would be best since it is an actual robot and not a simulation. This is because we cannot afford large amounts of exploration in our algorithm because every time it chooses particularly bad P, I and D values it will go off the track and we have to stop it by hand, which can become rather daunting over time. By using gradient descent, starting with known good values, it should keep this issue to a minimum, we predict that a gradient descent method will work quite well as we don't foresee multiple local minimums for error occurring.

Our implementation of simulated annealing requires some way of evaluating performance of each run. To do this we score each run by adding the lap time to the total error seen during the run. With this measure, runs with greater values are considered worse runs. With simulated annealing, we start with known decent values for P, I and D and explores by randomly selecting new values of P, I and D within a predefined range. Determined by:

P = bestP + n/d * rand(-annealP, annealP)

P_{n e w} =P_{b e s t} +italic " " {M a x R u n s - i} over {M a x R u n s} ∙r a n d \( -a n n e a l P ,a n n e a l P \)

For our simulated annealing algorithm, we set a range of values that the program can choose from for P, I and D in each run. If it chooses values that performs better, it updates the best known values and any new values chosen will be centered around the new value. If it chooses values that perform worse, those values are thrown out. If values are chosen that are so bad that the robot cannot stay on the track, it receives a bonus error of 100 each iteration plus any extra time that passes while robot is placed back on the path and is thus guaranteed not to be a candidate for the best run. Each run, the range of values it can choose from narrows around the current best, eventually converging at some set of values for P, I and D. The more runs that are given, the better the convergence will be. Due to memory constraints, our robot can only track 20 values to store it its history. Our algorithm does not require us to store these values, but we have to if we wish to show results from the run since outputting serial data while running causes the robot to act erratically.

This section should talk about the learning technique used to find PID values.
Error: Reference source not found
Error for each run will be calculated by using both the lap time and the sum of the absolute value of error over the entire run. We will score it with a bias toward speed over control by multiplying our speed to affect the score by 50% while allowing the error correction to account for 50%. The goal is the fastest lap-time possible, and any values of P, I, and D that cannot consistently keep the robot on the track will be thrown out.
Comparison between Controllers (1 page) F
One of the goals of this project is to produce a low error, fast time around the track. The goal of the previous experiments was to show the differences between the values of P, I, and D. The results are very interesting. Error: Reference source not found shows the top ten runs as determined by the scoring previously defined. The first interesting point is 3 of the top 5 runs have only the P and I component. The second interesting point is that a P controller out performs the PID controller. It appears that the slower the speed of the robot the less the D term is needed. Additionally, not a single PD controller ranked in the top 10. It seems that for a robot this small, lightweight, and slow that the P and D term only would suffice for good lap times with lower error. It would be interesting to see the manual tuned values for a robot that had faster motors. This is an area for improvement.

Run	P	I	D	Error	Time
1	20	0	0
2	20	0	10
3	20	0	15
4	20	0.05	0
5	20	0.05	10
6	20	0.05	15
7	20	0.1	0
8	20	0.1	10
9	20	0.1	15
10	25	0	0
11	25	0	10
12	25	0	15
13	25	0.05	0
14	25	0.05	10
15	25	0.05	15
16	25	0.1	0
17	25	0.1	10
18	25	0.1	15
19	30	0	0
20	30	0	10
21	30	0	15
22	30	0.05	0
23	30	0.05	10
24	30	0.05	15
25	30	0.1	0
26	30	0.1	10
27	30	0.1	15

 Table – Experiments with Different PID Values

Comparison of PID Values (1 page) J
During our initial runs without learning we have found some values of P, I, and D that work well and others that do not. We have tested our learning algorithm with known good values and known bad ones. During runs with known good values, most changes during the run are vaguely noticeable but a difference can be seen between some runs. If we start it with known bad runs such as a high P value, the robot is very shaky as it tries to over-correct it's error but its over-all error and speed are still quite good so it takes many iterations for it to learn a lower P or higher D to smooth out the shakiness. When started with a P that is too low, it cannot stay on the track most of the time and must be guided by hand. However, due to the penalties in place for leaving the track, it never learns any values that are worse than the current, and will fairly quickly begin to learn values of P that allow it to stay on the track without intervention.

The PID values found in the method section will be tested against the learned PID values. This will show the benefit of the learned PID values over the user set values.
# Conclusion (0.5 – 1 page) F J

# Conclusion
In conclusion, this project demonstrated the use of a PID controller to follow a line laid out by the user. It also opened the door to all of the problems that hardware brings with it. As a lessons learned, fixing the hardware problems that arose during the creation of this robot took longer than the software problems. Although this line following robot does well, it has many areas it is lacking such as low memory capacity, low processing power and lack of threading. This kept us from being able to save off data from the longer runs which would be needed to learn PID values well and kept us from being able to transmit data while the robot was learning. There are also some areas it could improve. One improvement in particular is that the microcontroller board used came with an onboard motor driver. This motor driver was unable to carry the power needed to drive the high speed motors we intended to use on the system which require higher current than our motor drivers can provide. The motors in combination with the subpar motor controller have yielded less than ideal results. Therefore, another improvement is to get faster motors. A side effect due to this change is less battery life, but with a rechargeable battery this shouldn’t be an issue.

 The learning technique outlined in this project showed signs of great improvement over the manual tuning process with respect to faster run, lower error, and most importantly with fewer manual interruptions of the learning process. This learning process is a real appealing feature for anyone who has had the pleasure of manually tuning a PID controller. There are some leading improvements that are required to have a viable learning machine. The first of which is a way to store the values of the best PID so that sequential runs can take place using the best value from the previous runs. In addition, switch should be added to allow for the robot to start in learning mode or performance mode. This would allow for the ?????

# References
Pololu Baby Orangutan B Users Guide. Available from http://www.pololu.com/docs/pdf/0J14/baby_orangutan_b.pdf.